## Slide 1
Clocks, Counters, and Timers
HCM - 2021

## Slide 2: Agenda
Clock sources
Basics of counters and timers
Clocks, counters, and timers in ARM Cortex-M chips
Labs

## Slide 3: Clock Signals
Clock signals are required for a lot of stuff
  CPU execution
  Internal communications, e.g., peripheral bus
  External communications, e.g., USB, USART
  Analog-to-digital conversion
  Tick generation for timers

## Slide 4: Counters and Timers
Counters and timers are ones of the most important components of MCUs
A counter keeps track of how many event ticks have occurred
A timer is a counter that counts deterministic clock cycles
Two terms are often used interchangeably

## Slide 5: Typical Uses of Counters/Timers
Scheduling future events
  One-shot events
  Periodic events
Input capture
  Measuring input pulse length
Output waveform generation
  Output compare – flags or toggles output pin when the counter reaches a certain value
  Pulse-width modulation (PWM) – generates
  analog output encoded as pulse length

## Slide 6: Basic Counter/Timer Operations

## Slide 7: Counter Modes
Up-counting
Down-counting
Center aligned (up/down)

## Slide 8: Prescaler
Divides clock frequency; increases timer period

## Slide 9: Input Capture
Measures input pulse lengths
Applications: decoding remote control signals, distance measurement

## Slide 10: Output Compare
Generates an event when counter matches a certain value
Possible MCU’s behavior when receiving a compare event:
  Sets a flag
  Generates an interrupt
  Sets, resets, or toggles output pin

## Slide 11: Pulse-Width Modulation (PWM)
PWM utilizes duty cycle control to simulate analog output
Applications: motor speed control, servo position control, LED brightness control

## Slide 12: PWM Waveform Generation
Typical MCU behavior
  Auto-reload event sets output pin high
  Output-compare event sets output pin low
Output compare value determines PWM duty

## Slide 13: STM32F4xx’s Timers
Basic timers: TIM6/TIM7
General-purpose timers: TIM2/TIM3 and TIM15/TIM16
Advanced timers: TIM1
Low-power timers: LPTIM

## Slide 14: STM32F4xx’s General-Purpose Timers

## Slide 15: Important Timer-Related Registers
TIMx->PSC (16 bits)
  Prescaler for TIMx
  PSC = 0  no prescaler (prescaler = 1)
  PSC = n  prescaler = n+1
TIMx->ARR (32 bits)
  Auto-reload register for TIMx
  Counter counts up to and including ARR
  Therefore, reload occurs every ARR+1 clock ticks
TIMx->CCRy (32 bits)
  Capture/compare register for TIMx, channel y

## Slide 16: Calculating Timer Period/Frequency
Let
  PSC = Prescaler (TIMx->PSC)
  ARR = Auto-Reload Register (TIMx->ARR)
Then
or

## Slide 17: Example: Timer Period
What is the timer’s period in milliseconds with the following configuration?
  Up-counting configuration
  Input clock: 80 MHz
  Prescaler (PSC): 999
  Auto-reload register (ARR): 4999

## Slide 18: PWM Modes 1 vs 2

## Slide 19: Calculating PWM Duty Cycle
Assume up-counting configuration and PWM mode 1
(output is clear when compare match)
Let
  ARR = Auto-Reload Register (TIMx->ARR)
  CCR = Capture/Compare Register (TIMx->CCRy)

## Slide 20: Example: PWM Duty Cycle
What is the PWM’s frequency and duty cycle with the following configuration?
  Up-counting configuration
  Input clock: 80 MHz
  Prescaler (PSC): 79
  Auto-reload register (ARR): 4999
  Capture/compare register (CRR): 2000
  PWM mode 1