## Slide 1
UART Module

## Slide 2: Agenda
UART Protocol
Operation
DMA
Example

## Slide 3: Universal Asynchronous Receiver and Transmitter (UART)
Universal
  UART is programmable ( data bits, stop bit, parity, …)
Asynchronous
  Sender provides no clock signal to receivers

## Slide 4: Connecting to PC
FT232R converts the UART port to a standard USB interface

## Slide 5: Data Frame
Sender and receiver uses the same transmission speed
  Data frame
  One start bit
  Data (LSB first or MSB, and size of 7, 8, 9 bits)
  Optional parity bit
  One or two stop bit

## Slide 6: Baud Rate
Historically used in telecommunication to represent the number of pulses physically transferred per second
In digital communication, baud rate is the number of bits physically transferred per second (9600, 115200)
Example:
  Baud rate is 9600
  Each frame: a start bit, 8 data bits, a stop bit, and no parity bit.
  Transmission rate of actual data
  9600/(1 + 8 + 1) = 960 bytes/second
  The start and stop bits are the protocol overhead

## Slide 7: Baud Rate
If OVER8 is 0, then the signal is oversampled by 16, and 4 bits are used for the fractional part.
If OVER8 is 1, then the signal is oversampled by 8, and 3 bits are used.
If BRR is 0x1BC and OVER8 is 0, then 0x1B is the integer part and 0xC is the fractional part.

## Slide 8: Baud Rate
Suppose the processor clock 𝑓𝑃𝐶𝐿𝐾 is 16MHz, and the system is oversampled by 16 (𝑂𝑉𝐸𝑅8 = 0),
Thus USARTDIV is 104.1875, which is encoded as 0x683, desired baud rate 9600

## Slide 9: Error Detection
Even Parity: total number of “1” bits in data -> parity is even
Odd Parity: total number of “1” bits in data -> parity is odd
  Example: Data = 10101011 (five “1” bits)
The parity bit should be 0 for odd parity and 1 for even parity
This can detect single-bit data corruption

## Slide 10: Transmitting 0x32 and 0x3C

## Slide 11: UART Connection

## Slide 12: Sending Data

## Slide 13: Receiving Data

## Slide 14: UART Interrupt: Sending & Receiving Data

## Slide 15: UART Interrupt: Receiving Data

## Slide 16: STM32 DMA
DMA: Direct Memory Access
  Peripheral  RAM
  RAM  RAM
TBD

## Slide 17: STM32 DMA: Block Diagram

## Slide 18: STM32 DMA Features
Dual AHB master bus architecture, one dedicated to memory accesses and one dedicated to peripheral accesses
Independent source and destination transfer width (byte, half-word, word): when the source and destination data widths are different
Independent Incrementing or Non-Incrementing addressing for source and destination. Possibility to set increment offset for peripheral address.

## Slide 19: DMA – Peripheral to Memory Mode

## Slide 20: DMA – Memory-to-Peripheral mode

## Slide 21: DMA – Memory-to-Memory mode

## Slide 22: FIFO: Data Packing/Unpacking

## Slide 23: FIFO: Threshold & Burst mode

## Slide 24: Circular & Double Buffer modes

## Slide 25: UART DMA: Receiving & Sending

## Slide 26: UART DMA: Receiving & Sending

## Slide 27: Voltage Levels

## Slide 28: Bluetooth

## Slide 29: Q&A