## Slide 1
INTERRUPTS
HCM - 2021

## Slide 2: Agenda
Polling vs. interrupt programming styles
General interrupt mechanism in microcontrollers
ARM Cortex-M4’s interrupt system

## Slide 3: Common Programming Patterns
Software polling
Interrupt (event-driven)
DMA (direct memory access)
  Good for moving large amount of data, e.g., audio
RTOS (Real-Time Operating System)
  Simplifies a complex application into smaller, concurrent tasks
Combination of methods above

## Slide 4: Polling vs. Interrupt
Polling
  Program keeps checking for a certain event to happen
  E.g. GPIO pin status changed, or timer
Interrupt
  Program keeps doing regular routines
  When an event of interest happens, the program suspends normal execution and executes code that handles the event

## Slide 5: Polling vs. Interrupt (cont’d)
Considering pseudo-code for switch-toggled LED

## Slide 6: Interrupts vs. Exceptions
An exception is an event that alters normal program flow
Interrupts are exceptions caused by hardware events, such as peripherals and I/O
Other exceptions are:
  Faults – caused by faulting instructions, such as division by zero
  Traps – deliberately caused by user program to trigger certain event or service
  Aborts – used only to signal severe problems; operation no longer possible

## Slide 7: Interrupt Service Routine (ISR)
A special block of code that gets executed automatically by the CPU when a corresponding interrupt occurs
Also known as Interrupt Handler
  or Exception Handler in general

## Slide 8: Maskable vs. Non-maskable Interrupts
Maskable interrupts can be disabled by the program
  To perform critical operations that must not be interrupted
  Most interrupts are maskable
Non-maskable interrupts cannot be disabled
  Used to indicate critical events, e.g., reset, power failure

## Slide 9: Locations of ISRs
Should be at fixed locations so CPU can find them easily
Problem: different ISRs have different lengths
Possible solutions
  A table of ISR locations (function address) is maintained at a fixed memory location
  This table is called Interrupt Vector Table
  ISRs may be changed dynamically by the application
  AVR’s vector table is filled with JMP instructions, while Cortex-M’s vector table stores ISR addresses

## Slide 10: Interrupt Priorities
Many MCUs support different interrupt priorities
An interrupt with a higher priority can preempt the execution of a lower-priority interrupt
Priorities may be fixed or programmable
Program can also choose to disable interrupts whose priorities are below a threshold

## Slide 11: Interrupt Latency
Interrupt latency amount of time to respond to an interrupt
Depends on:
  How long the interrupt is disabled
  Time to execute ISRs of higher priority interrupts
  Time for processor to stop current execution, do necessary save state, and start executing the ISR
  Time taken for the ISR to save context and start executing instructions that count as a ‘response’
Factor 3 depends on HW, not under software control
Other factors are controlled by writing efficient code that are not too long
  Make ISRs short

## Slide 12: Writing an ISR
ISR should finish as quickly as possible
ISR does not accept parameters, nor returns a value
  To communicate with the main program, use global variables or shared data structures
  These variables must be declared volatile
For events that need complicated handling, set a flag to notify the main code
Accessing variables shared with ISR must be atomic
  Especially read-modify-write memory update sequence
  An interrupt can happen in the middle of variable access
  Wrap these statements inside a critical section (disable interrupt, etc.)

## Slide 13: STM32F4’s Interrupt System
Controlled by Nested Vectored Interrupt Controller (NVIC)
67 maskable interrupt channels
16 programmable priority levels
  4 bits of interrupt priority are used
Low-latency exception and interrupt handling

## Slide 14: Cortex-M4’s Memory Map

## Slide 15: Data Memory

## Slide 16: Instruction Memory

## Slide 17: NVIC Operation
When an interrupt signal is detected, NVIC looks up the ISR address from the interrupt vector table
The address is then passed to the CPU

## Slide 18: Interrupt Vector Table

## Slide 19: Example: ISR Address
Find the interrupt vector table entry that contains the address of EXTI Line3 interrupt handler
EXTI Line3 interrupt’s position is 9
Entry address = 64 + 4*9 = 100 = 0x64
Notes: ISR address found in the table entry always has LSB
set to 1 to indicate THUMB instruction set

## Slide 20: Single Interrupt Operation

## Slide 21: Cortex-M4’s Interrupt Priorities
Four bits  16 different priorities
The four bits can be divided into
  Preemption priorities (0-4 bits)
  Sub priorities (0-4 bits)
An interrupt with smaller preemption priority number (higher priority) preempts the execution of an interrupt with larger preemption priority number
For pending interrupts of the same preemption priority, one with the smaller sub priority number will be serviced first

## Slide 22: Nested Interrupts: Preemption

## Slide 23: Nested Interrupts: Tail Chaining
Suppose EXTI4 is of lower priority than EXTI3
Cortex-M4 optimizes the unnecessary unstacking/stacking operations, saving clock cycles

## Slide 25: QUESTION ?