## Slide 1
ADC Module

## Slide 2: Agenda
ADC introduction
ADC Techniques
STM32F4 ADC

## Slide 3: Digital and Analog Signals
Digital signals
  Have a limited number of valid values
Analog signals
  Have a infinite number of values in a range
In the real world, most signals are available in analog form

## Slide 4: Digital/Analog Conversion
Analog-to-digital converter (ADC)
Digital-to-analog converter (DAC)

## Slide 5: Common DAC Techniques
PWM + low-pass filter
R-2R ladder
Integrated resistor string

## Slide 6: ADC Resolution
The higher the bit resolution, the more accurate the
conversion

## Slide 7: Quantization Error
Suppose #bits = 3; Δ = Vref/23 (aka. 1 LSB)

## Slide 8: Common ADC Techniques
Flash / half-flash
Successive approximation
Delta-sigma

## Slide 9: Flash ADC
Fastest ADC
Requires a large number of comparators and resistor (2n)

## Slide 10: Successive Approximation ADC
Or Successive Approximation Register (SAR)
Binary search - relatively fast and simple to implement

## Slide 11: SAR Operation

## Slide 12: Delta-Sigma ADC
Highest resolution; also slowest
Usually restricted to DC or audio frequencies

## Slide 13: Comparison of ADC Methods

## Slide 14: Minimum Sampling Rate
Nyquist Theorem
Input signals must also be properly filtered to eliminate
unwanted high-frequency components

## Slide 15: Voltage Calculation
Two variations, depending on ADC:
ADC value at full-scale voltage = 2n
ADC value at a full-scale voltage = 2n – 1
Vin = Input Voltage
ADC = Giá trị quy đổi
N = độ phân giải ( số bit)
Vref = điện áp tham chiếu
Xác định giới hạn đo <= VADC
1.8V, 2.5V, 3.3V

## Slide 16: STM32F4x’s Analog Components
1x 12-bit SAR ADC
  5.33 Msps max conversion rate with full resolution
  Up to 10 external channels and 4 internal channels
  Analog watchdog
  Single-ended and differential mode inputs
  Dual clock domain architecture
2x DAC

## Slide 17: Analog Input Sources

## Slide 18: ADC Clock Sources
Selectable from two clock domains

## Slide 19: ADC Measurement Time
n  resolution (number of bits) – effective bits = n - 2
Minimum of 2.5 ADC_CLKs for Tsampl
Minimum of 12.5 ADC_CLKs for Tconversion (12-bit resolution)
Hence, 5.33 Msps for 80 MHz ADC clock frequency

## Slide 20: Choosing Sampling Time

## Slide 21: Conversion Modes

## Slide 22: ADC – Timing Diagram

## Slide 23: Q&A