## Slide 1
Cortex-M4 System Timer
HCM - 2021

## Slide 2: Agenda
Overview
Hardware diagram
Registers
Example code

## Slide 3: Overview
Generate SysTick interrupts at a fixed time interval
Example Usages:
  Measuring time elapsed, such as time delay function
  Executing tasks periodically, such as periodic polling, and OS CPU scheduling
Fixed time interval
time
SysTick interrupts

## Slide 4: System Timer (SysTick)
System timer is a standard hardware component built into ARM Cortex-M.
This hardware periodically forces the processor to execute the following ISR:
void SysTick_Handler(void){
...
}
Processor
Core
NVIC
Peripherals
I/O pins
IRQs
IRQs
System
Exceptions
System Timer
SysTick IRQ
ARM Cortex-M
Microcontroller

## Slide 5: Diagram of System Timer (SysTick)
Counter
Reload Value
24-bit down counter
Is it zero?
Yes
copy

## Slide 6: System Timer Operation
SysTick Interrupt
SysTick Interrupt
SysTick Interrupt

## Slide 7: Diagram of System Timer (SysTick)
Set COUNTFLAG to 1
Counter
Reload Value
24-bit down counter
Is it zero?
Yes
copy
SysTick control and status register (SysTick_CTRL)

## Slide 8: Diagram of System Timer (SysTick)
Counter
Reload Value
AHB Clock
24-bit down counter
Is it zero?
Yes
copy
/8
0
1
SysTick control and status register (SysTick_CTRL)
AND
External clock
Processor clock
Set COUNTFLAG to 1

## Slide 9: Registers of System Timer
  SysTick reload value register (SysTick_LOAD)
  SysTick current value register (SysTick_VAL)
SysTick calibration register (SysTick_CALIB)
  SysTick control and status register (SysTick_CTRL)

## Slide 10: Registers of System Timer
24 bits, maximum value 0x00FF.FFFF (16,777,215)
Counter counts down from RELOAD value to 0.
Writing RELOAD to 0 disables SysTick, independently of TICKINT
Time interval between two SysTick interrupts
If 100 clock periods between two SysTick interrupts
  SysTick reload value register (SysTick_LOAD)
Interval = (RELOAD + 1) × Source_Clock_Period
RELOAD = 99

## Slide 11: Registers of System Timer
Reading it returns the current value of the counter
When it transits from 1 to 0, it generates an interrupt
Writing to SysTick_VAL clears the counter and COUNTFLAG to zero
  Cause the counter to reload on the next timer clock
  But, does not trigger an SysTick interrupt
It has random value on reset.
  Always clear it before enabling the timer
  SysTick current value register (SysTick_VAL)

## Slide 12: Registers of System Timer
A read-only register
TENMS (10 ms) holds the reload value, which will yield a 10ms period
May not be implemented or may be defined differently by chip designers
SysTick calibration register (SysTick_CALIB)

## Slide 13: Example Code
void SysTick_Initialize (uint32_t ticks) {
SysTick->CTRL = 0; // Disable SysTick
SysTick->LOAD = ticks - 1; // Set reload register
// Set interrupt priority of SysTick to least urgency (i.e., largest priority value)
NVIC_SetPriority (SysTick_IRQn, (1<<__NVIC_PRIO_BITS) - 1);
SysTick->VAL = 0; // Reset the SysTick counter value
// Select processor clock: 1 = processor clock; 0 = external clock
SysTick->CTRL |= SysTick_CTRL_CLKSOURCE;
// Enables SysTick interrupt, 1 = Enable, 0 = Disable
SysTick->CTRL |= SysTick_CTRL_TICKINT;
// Enable SysTick
SysTick->CTRL |= SysTick_CTRL_ENABLE;
}

## Slide 14: Implementing Delay Function
volatile int32_t TimeDelay;
int main (void {
SysTick_Initialize(1000); // Interrupt period = 1000 cycles
Delay(100); // Delay 100 ticks
...
}
void SysTick_Handler (void) { // SysTick interrupt service routine
if (TimeDelay > 0) // Prevent it from being negative
TimeDelay--; // TimeDelay is a global volatile variable
}
void Delay (uint32_t nTime) {
// nTime: specifies the delay time length
TimeDelay = nTime; // TimeDelay must be declared as volatile
while(TimeDelay != 0); // Busy wait
}

## Slide 15: Calculating Reload Value
Suppose clock source = 80MHz
Goal: SysTick Interval = 10ms
What is RELOAD value?

## Slide 16: Question ?